## Slide 1: WiMax
Telephone and cable companies provide wired access to the Internet for homes and offices
Today everything changed from wired to wireless because of two reasons
  Wired access is not available and even available it is expensive
  People need to access the Internet when they are using cellular phones
  WiMAX is an IP based, wireless broadband access technology that provides performance similar to 802.11/Wi-Fi networks with the coverage and QOS (quality of service) of cellular networks. WiMAX is also an acronym meaning "Worldwide Interoperability for Microwave Access (WiMAX).

## Slide 2
WiMAX (Worldwide Interoperability for Microwave Access) is a telecommunications protocol that provides fixed and mobile Internet access. The name "WiMAX" was created by the WiMAX Forum, which was formed in June 2001 to promote conformity and interoperability of the standard. The forum describes WiMAX as "a standards-based technology enabling the delivery of last mile wireless broadband access as an alternative to cable and DSL".
16.1.1 Services
WiMAX provides two types of services
  Fixed
  Mobile

## Slide 3
Fixed WiMax :
A base station can use different types of antenna like omnidirectional, sector or panel to optimize the performance
WiMAX uses a beamsteering adaptive antenna system (AAS)
During transmission, it focuses its energy in the direction of the subscriber
While receiving , it focus in the direction of the subscriber station to receive maximum energy sent by the subscriber
Fixed service is similar to telephone network or wired connection network
WiMax also uses MIMO antenna system, which can provide simultaneous transmission and receiving functions
Please see the diagram from the text book

## Slide 4
Mobile WiMax
It is same as fixed service except the subscribers are mobile stations that move from one place to another
The same issue is involved in cellular telephone system, such as roaming
Please see the figure from textbook
16.1.2 IEEE project 802.16
Standard IEEE 802.11 is wireless LAN
  Distance between a base station and a host in 802.11 is very limited
  Defines connectionless communication
Standard IEEE 802.16 is a standard for a wireless WAN (or MAN)
  distance between a base station and subscriber station may be separated by 10s of kilometer
  Defines connection oriented service

## Slide 5
IEEE 802.16
  Two revision happened
  802.16d :which concentrates on the fixed WiMax
  802.16e: which defines the mobile WiMax
16.1.3 : Layers in project 802.16
Service specific convergence sub layers
MAC sub layers
Security sub layers
Data link layer
Transmission convergence sublayers
Physical medium dependent sublayers
Physical layer

## Slide 6
Layers in project 802.16
Service specific convergence sublayers
  It is for broadband wireless communication
  It is devised for connection oriented service in which each connection may benefit from specific QOS
MAC sublayers
  Defines access method and the format of the frame
  It is the sublayer designed for connection oriented service
  The packets are routed from base station to the subscriber station using connection identifier
Access method
  WiMax uses reservation scheduling access method
  Base station needs to make a slot reservation before sending a slot size of data to a subscriber station
  Subscriber station need to reserve slot and before sending a slot size of data to the base station

## Slide 7
Frame format
WiMax generic frame format
3bytes 2 B 1B variable 4B
1bits 1 6 1 1 2 1 11
First bit is the frame identifier . If 0 it is generic frame. If 1 it is control frame
EC: encryption control . Denotes whether encryption is required or not for security purpose. If the bits is 0, it means no encryption, if it is 1, it means needs encryption at the security sublayers
Combination of fields | Connection ID | header CRC | Payload Upto 2038bytes | CRC
0 | EC | TYPE |  | CI | EK |  | LENGTH

## Slide 8
Type : it indicates the type of frame, it is used only for generic frame. It mainly used to indicate type of payload (packed load or fragmented load)
CI: checksum ID is used to indicate frame checksum field should be present or not . If the payload is multimedia, forward error correction is applied to the frame and there is no need for checksum
EK: encryption key (2bits) defines 4 keys for encryption (if required)
Length: (11 bits) defines the total length of the frame. This field is present in generic frame and is replaced by the bytes needed in control frame

## Slide 9
WiMax control frame format
1 B 2B 2B 1B
1b 1b 6b
Bytes needed: 16bits size , defines the number of bytes needed for allocated slots in the physical layer
Connection ID: (16bits), defines the connection identifier for the current connection. IEEE 802.16 and WiMax define a connection-oriented protocol
Header CRC: (8bit header CRC). Is used to check whether header is corrupted. It uses 8 bit polynomial
Payload: variable length, defines payload , the data is encapsulated in the frame (frame from service specific convergence sublayer). This field is not present in the control frame
CRC : is used for error detection over the whole frame. It uses the CRC 32 bit divisor
Three fields | Bytes needed | Connection ID | Header CRC
1 | 0 | type

## Slide 10
Addressing :
Each subscriber and base station has a 48bits MAC address
But these addresses are not there in the frame format
Both src and des address are mapped to connection identifier during connection establishment phase.
Connection identifier is a virtual connection identifier (VCI)
Each frame uses the same VCI throughout the session during data transfer
Protocol offers connection-oriented service
Security sublayer
1. The Last sublayer in the data link layer provides security form communication
2. It takes care of encrypting the information exchanged between subscribesr and base station

## Slide 11
Transmission convergence sublayer
Uses TDD time division duplex (bidiretional)
Physical layer packs the frame received from the DLL into two subframes
  One frame carries data from base station to the subscriber (downstream)
  Another frame carries data from the subscriber to the base station(upstream)
  Each subframe is divided into slots
Dr Downstream Reservation , D-downstream data
UR Upstream reservation , C-control , U-Upstream data
CR-means request
DR | UR | D1 | D2 | ......... | DN | C | CR | U1 | U2 | .... | UN

## Slide 12
Physical medium dependent sublayer
1. original IEEE 802.16 defined the band 10-66GHZ and modulations QPSK (2bits/baud), QAM-16 (4bits/baud) and QAM(6bits/baud) for long, medium and short distance communication
2. IEEE defined 802.16d (fixed WiMax) which added the band 2-11 GHZ using orthogonal frequency division multiplexing OFDM
3. IEEE defined 802.16e (mobile WiMax) and added scalable orthogonal FDM (SOFDM)